Sealoflex combination debuts on UK car park

Ever increasing traffic intensities, higher axle loads and tyre pressures and unfavourable wheel configurations result in increasing deterioration of asphalt pavements.

Pavement performance can be improved by improving the properties of asphalt mixes. The best improvements are obtained by incorporating specific polymers to the asphalt binder.

Sealoflex comprises a group of polymer modified asphalt binders for use in heavy duty asphalt pavements. It is also suitable as a binder in bituminous rich mixes such as porous asphalt and stone mastic asphalt, without the need of any anti drain down agents. Asphalt concrete with Sealoflex binders can be produced in any hot mix plant, and can be used in all pavement layers. The composition of the mix can comply with statutory regulations.

July saw the start of a contract to lay approximately 50,000m² of GridSeal® at London’s Heathrow airport on the Pink Elephant Car Park, reputedly the largest car park in Europe.

This is the first use in the UK of GridSeal®, a combination of GlasGrid® and Sealoflex SC-33, a system that has been successfully used to reduce reflective cracking in asphalt overlays throughout Europe, the Middle East, Far East and Australia since 1990.

Consultants Project Techniques were faced with a common difficulty of providing a thin flexible overlay system over a concrete base with the client’s requirement to minimise reflective cracking. The system chosen after in depth technical consultations and fierce competition was GridSeal® which is a combination of GlasGrid® 8550 with tensile strength 50kN/m in each direction and Sealoflex SC-33 a hot sprayed polymer modified binder at 1.7kg/m² rate of spread. This combination is finally overlaid with 10mm chippings to keep paving traffic aware from the highly adhesive binder layer.

Asphalt Reinforcement Services Ltd, UK distributors, is operating as main sub-contractor to Ringway and Material Edge Ltd UK, representative of Ooms Avenhorn Holding, the manufacturer of Sealoflex SC-33. The registered owners of the GridSeal® are responsible for the spraying of Sealoflex SC-33. This specialist binder requires a specialised surface dressing spray tanker that can spray highly polymerised binders at up to 200°C.

For this project Ooms Avenhorn Holding contractor arm Ooms Producten provided sub-contracted supply and laying of the Sealoflex SC-33 to Asphalt Reinforcement Services.

On the first visit approximately 11,000m² of GlasGrid® was laid with a special laying machine by ARS Ltd in about five hours the day before the Sealoflex SC-33 was laid. Overnight rain did not affect the grid which remained adhered to the surfacing through its contact adhesive. The surface was dry by the morning and spraying of the hot PMB took about three hours with chipping a further two hours.

The chippings keep the paving traffic away from the highly adhesive binder layer and provide an excellent key into the overlay which in this case was a 10mm SMA specification design to provide good skid resistance and low scuffing under power assisted steering from parking cars.

The asphalt overlay design provides a smooth well drained surface for car parking over an area of concrete including some spalled joints and fractured PCC slabs that was previously Heathrow Airport taxiway.

Commencing with a layer of approximately 20mm of regulating onto which the GridSeal® system is applied the whole area is being overlaid with 40mm minimum thickness of SMA surfacing by the main contractor Ringway.

Published in World Highways, July/August 2005 (Bitumen Technology)